## Slide 1: Setting up Instrument Interchangeability with IVI Drivers
Public Material
Last Modified August 22, 2011

## Slide 2: Overview
IVI drivers are quite straightforward to use. You first install the Agilent IO Libraries Suite, install your IVI driver, then write your application using the IVI driver. You tell the IVI driver which instrument you want to use by specifying the instrument’s VISA address in the Initialize call. No magic, it just works, its simple.
However, IVI allows you to get a little more fancy. With a little bit of configuration you can write one set of code (using IVI Class Compliant calls), that is able to control different instrument models (e.g. different DMM’s), even from different vendors. Interested? Read on…

## Slide 3: Overview continued…
To achieve this goal of Interchangeability of different instruments, we need to setup some configuration mappings in a database called the IVI Configuration Store, which is installed by popular I/O libraries such as the Agilent IO Libraries Suite and NI VISA. We then have to configure the IVI Configuration Store and tell it which instruments we want to use, and which IVI drivers we have for those instruments.
The key mappings that we need to use are the following:
Logical Name
Driver Session
Software Module
Hardware Asset

## Slide 4: Overview continued…
While Agilent provides IVI drivers that support Class Compliant functionality and Interchangeability, we don’t provide a tool to view/edit the IVI Configuration Store. To make changes to the IVI Configuration Store, you will need to access it in one of the following ways:
NI provides an IVI Configuration Store editor as part of their NI IVI Compliance Package, which you can download from www.ni.com. You can find instructions on how to use the editor in NI’s IVI Driver Help topic “Overview-Configuring IVI Instruments Using MAX”
The Mathworks provides a tool call Test and Measurement Tool (tmtool) as part of their Instrument Control Toolbox. You can find out more about this tool at http://www.mathworks.com/help/toolbox/instrument
The IVI Foundation provides an API called the IVI Config Server which allows you to make changes to the IVI Configuration Store.

## Slide 5: IVI Configuration Store Item relationships
IVI Config Store
Logical Name
Driver Session
Hardware Asset
Software Modules
Logical Name
the “name” that you provide in your programs when you call Initialize
Driver Session
connects the Hardware Asset and Software Module that you want to use for this configuration. It also lets you specify attributes, like “simulation”, that you want to use for this configuration.
Software Module
the list of installed IVI drivers and information about those drivers, such as which instrument models are supported
Hardware Asset
specifies the VISA address of an actual instrument

## Slide 6: A Simple Example
Suppose we have the following situation:
a 34401A DMM connected with GPIB at VISA address GPIB0::23::INSTR (we got this address from Agilent Connection Expert)
We have installed the 34401A IVI driver (www.agilent.com/find/ivi)
We don’t care about any of the “special” configuration options for IVI drivers

## Slide 7: 1) Configure Hardware Asset
First we’ll configure the Hardware Asset
We’ll give it a name of 34401Hardware
And we’ll specify the address GPIB0::23::INSTR
IVI Config Store
Logical Name
Driver Session
Hardware Asset
Software Modules

## Slide 8: 2) Decide which Software Module to use
We’ll then look for which Software Module (IVI driver) that we need to use
Looking in the list of supported Models for each Software Module, we can see that the Ag34401 supports the 34401A DMM
IVI Config Store
Logical Name
Driver Session
Hardware Asset
Software Modules

## Slide 9: 3) Create the Driver Session
We’ll give our Driver Session the name 34401Session
We’ll tell it to use the Software Module Ag34401
Then we’ll set the Hardware Asset to 34401Hardware
IVI Config Store
Logical Name
Driver Session
Hardware Asset
Software Modules

## Slide 10: 4) Create a Logical Name
Finally, we’ll create a Logical Name that we can pass to the Initialize call in our program
We’ll give our Logical Name the name DMM
We’ll also tell our new Logical Name to use Driver Session 34401Session
IVI Config Store
Logical Name
Driver Session
Hardware Asset
Software Modules

## Slide 11: Why go to all the trouble?
And that’s it!
We can now use our Logical Name in our program to talk to actual hardware, but why go to all the trouble when we could have just given the VISA address directly to the Initialize call?.
Consider the example where:
you may have several different types of DMM’s, such as a 34401A and a 34410A
you have written your code so that it only uses the IVI Class Compliant calls (IVI DMM in this case)
you want to be able to use the same code regardless of the instrument that is at the bench

## Slide 12: How to set it up
We’ll use the same setup we had in the first example for the 34401A, i.e.:
Hardware Asset pointing to GPIB0::23::INSTR with the name 34401Hardware
Software Module named Ag34401
Driver Session named 34401Session

## Slide 13: How to set it up, continued…
Then we’ll setup the 34410A with the following information:
Hardware Asset pointing to TCPIP0::156.140.113.220::inst0::INSTR with the name 34410Hardware
Software Module named Ag34410
Driver Session with the name 34410Session

## Slide 14: Final configuration
To change which instrument my application will use, I only have to change which Driver Session is assigned to the Logical Name that I am using in my program.
IVI Config Store
DMM (Logical Name)
34401Session (Driver Session)
34401Hardware (Hardware Asset)
Ag34401 (Software Module)
34410Session (Driver Session)
34410Hardware (Hardware Asset)
Ag34410 (Software Module)

## Slide 15: Conclusion
For more information, visit www.agilent.com or contact our Technical Contact Center at www.agilent.com/find/contactus
To download the latest version of Agilent IO Libraries Suite, visit:
www.agilent.com/find/iosuite
To download the latest IVI driver for your instrument, visit:
www.agilent.com/find/ivi